## Slide 1: Efficient Implementation of Multi-Center Potential Models in Molecular Dynamics with Cuda
Andreas Kirsch
Notes: Based on MarDyn
Kai Orend’s “Numerische Aspekte bei Molekulardynamik-Simulationen - Beschleunigung durch Graphikkarten” http://www5.in.tum.de/pub/orend2010.pdf

## Slide 2: Molecule Interactions
One molecule can be made up of multiple sites
Different potentials possible for the sites: Lennard-Jones, Charges, Dipoles
Interactions need to be calculated between all molecule pairs
Simplification: use a cutoff radius to reduce the number of interactions
Result: Linked Cell Algorithm

## Slide 3: Modules and Dependencies

## Slide 4: Performance (lj1)
Chart: Cutoff Radius
| 5 | 10 | 15 | 20 | 30
CPU A | 7.3037 | 57.03 | 203.9902 | 689.8876 | 1828.002
CPU B | 7.6504 | 59.0267 | 217.9113 | 983.5305 | 2640.706 | 9042.746
Thread Block 1 Warp | 2.485 | 4.4111 | 11.1143 | 33.4653 | 144.9458 | 1092.62
Thread Block 8 Warps | 4.9185 | 5.7503 | 12.9891 | 36.926 | 103.6058 | 460.4783
Warp Block 8 Warps | 6.1425 | 4.0531 | 8.8355 | 22.9172 | 67.816 | 245.5409 | 530.8878
Warp Block 16 Warps | 6.6488 | 4.2233 | 9.2224 | 23.4147 | 71.5977 | 250.2873 | 465.1414
Notes: Explain thread block and warp block processor

## Slide 5: Performance (lj2d1)
Chart: Cutoff Radius
| 5 | 10 | 15 | 20 | 30 | 40
CPU B | 4.9869 | 35.1235 | 121.8083 | 413.2992 | 1358.281 | 4439.128
Thread Block | 3.072 | 8.7377 | 25.1308 | 74.4362 | 344.2073 | 1961.119
Warp Block | 5.5389 | 5.361 | 14.4017 | 37.6498 | 125.7666 | 417.8133

## Slide 6: Thread Block Cell Processor
Notes: Draw a CUDA architecture diagram to explain thread blocks and warp blocks
Fixed thread block size for all cells -> not good for sparse domains
Only useful for high densities

## Slide 7: Warp Block Cell Processor
Dynamic scheduler
Jobs queue
No instruction-level synchronization
Memory-level synchronization (via spin locks)
Notes: Draw diagram that shows how WBCP works
Including dynamic job scheduling

## Slide 8: Optimizations
Shared memory cache
Constant memory
Non-interleaved storage
Notes: Shared memory results differ for TBCP and WBCP
Constant memory was a good idea
Non-interleaved storage failed because of temporarily sparse access patterns (more cache misses with non-interleaved data)
TODO: fully interleaved molecule storage

## Slide 9: Architecture/Implementation
Notes: *Global constant variables to avoid kernel parameters
*Heavy use of template parameters to link modules together and keep things interchangable
----! CUDA/C++ still sucks for fast, modular code
* 3 source code iterations during the project

## Slide 10: Interesting Papers
Better performance at lower occupancy http://www.cs.berkeley.edu/~volkov/volkov10-GTC.pdf
Demystifying GPU microarchitecture through microbenchmarking http://www.stuffedcow.net/research/cudabmk
CudaDMA: Optimizing GPU Memory Bandwidth via Warp Specialization http://www.stanford.edu/~mebauer/pdfs/cudadma-sc11.pdf

## Slide 11: Interesting Bugs & Facts
Constructors can be evil (for shared memory objects)
Too many nested, inlined loops confuse the compiler: __noinline__ to the rescue!
__syncthreads() should be called __syncwarps()!
PTX assembly has more “features”
Notes: PTX reduction and enhanced synchronization instructions

## Slide 12
Thank You!